## Slide 1: Computer Architecture Experiment
Topic 5. Dynamically Scheduled Pipelines using Scoreboarding
浙江大学计算机学院
2021年11月
Notes: 同学们好，今天我们讲一下实验5，这个实验主要是实现一个简单的浮点数流水线

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Checkpoints

## Slide 3: Experiment Purpose
Understand the principle of piplines that support multicycle operations.
Master the design methods of piplines that support multicycle operations.
Master verification methods of pipelined CPU supporting multicycle operations.

## Slide 4: Experiment Task
Redesign the pipelines with IF/ID/FU/WB stages and FU stage supporting multicycle operations.
Redesign of CPU Controller.
Verify the Pipelined CPU with program and observe the execution of program.

## Slide 5
Notes: 这是整个系统的结构图
浮点数流水线中分成了4个stage, IF/ID/FU/WB
IF阶段取指令，ID阶段decode, FU阶段进行计算，计算单元有branch, 整数的，浮点乘法，浮点除法，load/store memory的。
最后，writeback

## Slide 6: Control Unit
input clk,
input rst,
input[31:0] inst,
input valid_ID,
input ALU_done,
input MEM_done,
input MUL_done,
input DIV_done,
input JUMP_done,
input cmp_res_FU,
// IF
output reg_IF_en, branch_ctrl,
// ID
output reg_ID_en, reg_ID_flush,
output[2:0] ImmSel,
output ALU_en, MEM_en, MUL_en, DIV_en, JUMP_en,
// FU
output[3:0] JUMP_op,
output[3:0] ALU_op,
output ALUSrcA,
output ALUSrcB,
output MEM_we,
// WB
output reg[2:0] write_sel,
output reg[4:0] rd_ctrl,
output reg reg_write
Notes: 然后我们来看一些关键单元的代码
首先是ctrl unit,这个control unit贯穿全局
需要控制IF的stall和下一条指令的选择
控制ID的stall，flush, 立即数，根据指令类型判断计算所需要的计算单元，就是这里的ALU_en, MEM_en, MUL_en, DIV_en, JUMP_en
控制Fu阶段计算的操作数和操作类型
控制Wb阶段的写回，要不要写回，写回到什么寄存器，写回的数据数据：来自ALU,MEM, MUL, DIV, JUMP等
再看ctrl unit的输入，有指令，然后Fu计算完成之后，要给ctrl unit信号
[回到上一下ppt],然后再来看Fu阶段的这些计算单元

## Slide 7: FU-ALU
reg[3:0] Control;
reg[31:0] A, B;
always@(posedge clk) begin
  if(EN & ~state) begin // state == 0
    A ...
    B ...
    Control ...
    state <= 1;
  end
  else state <= 0;
end
...
module FU_ALU(
  input clk, EN,
  input[3:0] ALUControl,
  input[31:0] ALUA, ALUB,
  output[31:0] res,
  output zero, overflow,
  output finish
);
reg state;
assign finish = state == 1'b1;
initial begin
state = 0;
end
Notes: 首先来看ALU
整数计算单元
首先定义了一个state寄存器，用state寄存器来指示这个计算单元的占用状态和是否结束。
在ALU里面，两个操作数是A和B，执行的操作是由Control信号指定的
指令进入ALU单元进行计算，在初始状态，也就是这里的EN & ~state这里 (表明ALU使能，并且ALU空闲)，要对A，B，Control进行赋值，A要赋值为ALUA, B要赋值为ALUB，Control要赋值为ALU_Control
然后ALU就会计算出结果。
ALU计算是组合电路，立刻就能结束。同时，这个state转移到1，表明finish
在下一个时钟周期，state转移到0,表明ALU现在处于空闲状态

## Slide 8: FU-Multiplier
module FU_mul(
  input clk, EN,
  input[31:0] A, B,
  output[31:0] res,
  output finish
);
reg[6:0] state;
assign finish = state[0] == 1'b1;
initial begin
state = 0;
end
reg[31:0] A_reg, B_reg;
always@(posedge clk) begin
  if(EN & ~|state) begin
    A_reg ...
    B_reg ...
    state <= 7'b100_0000;
  end
  else state <= {1'b0, state[6:1]};
end
wire[63:0] mulres;
multiplier mul(.CLK(clk),.A(A_reg),.B(B_reg),.P(mulres));
assign res = mulres[31:0];
endmodule
Notes: 在Multiplier里面，同理
浮点数乘法计算需要7个时钟周期
这里用了一个7位寄存器的state
进入计算时，state最高位被置位为1
然后每个时钟周期，把这个1向右移动一位，state最低位为1时计算结束

## Slide 9: FU-Divider
module FU_div(
  input clk, EN,
  input[31:0] A, B,
  output[31:0] res,
  output finish
);
wire res_valid;
wire[63:0] divres;
reg state;
assign finish = res_valid & state;
initial begin
state = 0;
end
reg A_valid, B_valid;
reg[31:0] A_reg, B_reg;
always@(posedge clk) begin
  if(EN & ~state) begin // state == 0
    A_reg...
    B_reg...
    A_valid ...
    B_valid ...
    state ...
  end
  else if(res_valid) begin
A_valid ...
    B_valid ...
    state ...
  end
end
divider div(.aclk(clk),
  .s_axis_dividend_tvalid(A_valid),
  .s_axis_dividend_tdata(A_reg),
  .s_axis_divisor_tvalid(B_valid),
  .s_axis_divisor_tdata(B_reg),
  .m_axis_dout_tvalid(res_valid),
  .m_axis_dout_tdata(divres)
);
assign res = divres[63:32];
endmodule
Notes: 然后是除法
FU-div里面state只有一位
因为这里divider计算结束时会发出res_valid信号

## Slide 10: FU-Jump
module FU_jump(
  input clk, EN, JALR,
  input[2:0] cmp_ctrl,
  input[31:0] rs1_data, rs2_data, imm, PC,
  output[31:0] PC_jump, PC_wb,
  output cmp_res, finish
);
reg state;
assign finish = state == 1'b1;
initial begin
state = 0;
end
reg JALR_reg;
reg[2:0] cmp_ctrl_reg;
reg[31:0] rs1_data_reg, rs2_data_reg, imm_reg, PC_reg;
always@(posedge clk) begin
  if(EN & ~state) begin // state == 0
    JALR_reg ...
    cmp_ctrl_reg ...
    rs1_data_reg ...
    rs2_data_reg ...
    imm_reg ...
    PC_reg ...
    state ...
  end
  else state <= 0;
end
cmp_32 cmp ... add_32 a ... add_32 b ...
Notes: 后面这几个都差不多，大家可以自己看一下

## Slide 11: FU-Mem
module FU_mem(
  input clk, EN, mem_w,
  input[2:0] bhw,
  input[31:0] rs1_data, rs2_data, imm,
  output[31:0] mem_data,
  output finish
);
reg[1:0] state;
assign finish = state[0] == 1'b1;
initial begin
state = 0;
end
reg mem_w_reg;
reg[2:0] bhw_reg;
reg[31:0] rs1_data_reg, rs2_data_reg, imm_reg;
always@(posedge clk) begin
  if(EN & ~|state) begin
mem_w_reg ...
bhw_reg ...
rs1_data_reg ...
rs2_data_reg ...
imm_reg ...
    state ...
  end
  else state ...
end
wire[31:0] addr;
add_32 add ...
RAM_B ram(.clka(clk),.addra(addr),.dina(rs2_data_reg),.wea(mem_w_reg),
.douta(mem_data),.mem_u_b_h_w(bhw_reg));
endmodule

## Slide 12: Write Back
// WB
REG32 reg_WB_ALU(.clk(debug_clk),.rst(rst),.CE(FU_ALU_finish),.D(ALUout_FU),.Q(ALUout_WB));
REG32 reg_WB_mem(.clk(debug_clk),.rst(rst),.CE(FU_mem_finish),.D(mem_data_FU),.Q(mem_data_WB));
REG32 reg_WB_mul(.clk(debug_clk),.rst(rst),.CE(FU_mul_finish),.D(mulres_FU),.Q(mulres_WB));
REG32 reg_WB_div(.clk(debug_clk),.rst(rst),.CE(FU_div_finish),.D(divres_FU),.Q(divres_WB));
REG32 reg_WB_jump(.clk(debug_clk),.rst(rst),.CE(FU_jump_finish),.D(PC_wb_FU),.Q(PC_wb_WB));
MUX8T1_32 mux_DtR(... .o(wt_data_WB));
Regs register(...
.Wt_addr(rd_ctrl),.Wt_data(wt_data_WB),
...);
Notes: 最后是Writeback
Fu里面计算单元计算出来的结果会放到对应的寄存器，然后通过一个多路选择器写回寄存器

## Slide 13: Pipelines resolving Data Hazards
Notes: 讲完这些之后，和之前的5-stage pipeline一样，在浮点数流水线里面，也要处理data hazard和control hazard
在这个实验里面，一条指令FU和WB都执行完了，他的下一条指令才能进入FU，这样就不会出现data hazard

## Slide 14: Methods of resolving Control hazards
Predict-not-taken
Condition and Addr. Calculation in FU
Notes: 对于control hazard, 这个实验里面我们采用predict-not-taken, 和以前一样。
不一样的是，在这里，分支是在EXE阶段处理的，也就是FU-Jump处理的
在predict-not-taken的情况下，如果分支实际上take了，就需要kill两条指令
这个图可能不太对，Fu处理完就会flush

## Slide 15: Predict Untaken
assign branch_ctrl = (B_in_FU & cmp_res_FU) | J_in_FU;
assign reg_ID_flush = branch_ctrl;
MUX2T1_32 mux_IF(
  .I0(PC_4_IF),
  .I1(PC_jump_FU),
  .s(branch_ctrl),
  .o(next_PC_IF)
);
FU_jump ju(.clk(debug_clk),.EN(FU_jump_EN),.finish(FU_jump_finish),
.JALR(Jump_ctrl[3]),.cmp_ctrl(Jump_ctrl[2:0]),.rs1_data(rs1_data_ID),.rs2_data(rs2_data_ID),
.imm(Imm_out_ID),.PC(PC_ID),.PC_jump(PC_jump_FU),.PC_wb(PC_wb_FU),
.cmp_res(cmp_res_FU));
Ctrl Unit
IF Stage
FU_Jump
else if(flush) begin
  PCurrent_ID <= PCOUT;
  IR_ID <= 32'h00000013;
  valid <= 0;
end
ID Stage
Notes: 看一下代码
首先分支指令在FU_Jump，FU_jump判断分支是否会跳转，这个结果会存在cmp_res_FU
cmp_res_FU会传到ctrl unit,
如果是条件分支指令并且分支结果是会跳转，或者是无条件跳转的，branch_ctrl信号会置1，
If阶段，会根据branch_ctrl信号选择执行的下一条指令，Id阶段会进行flush

## Slide 16: Instr. Mem.(1)
NO. | Instruction | Addr. | Label | ASM | Comment
0 | 00000013 | 0 | __start: | addi x0, x0, 0 | 
1 | 00402103 | 4 |  | lw x2, 4(x0) | 
2 | 00802203 | 8 |  | lw x4, 8(x0) | 
3 | 004100b3 | C |  | add x1, x2, x4 | 
4 | fff08193 | 10 |  | addi x3, x1, -1 | 
5 | 00c02283 | 14 |  | lw x5, 12(x0) | 
6 | 01002303 | 18 |  | lw x6, 16(x0) | 
7 | 01402383 | 1C |  | lw x7, 20(x0) | 
8 | 40220433 | 20 |  | sub x8,x4,x2 | 
9 | ffd50493 | 24 |  | addi x9,x10,-3 | 
10 | 00520c63 | 28 |  | beq x4,x5,label0 | 
11 | 00420a63 | 2C |  | beq x4,x4,label0 | 
12 | 03000a13 | 30 |  | addi x20,x0,48 | 
13 | 03400a13 | 34 |  | addi x20,x0,52 | 
14 | 03800a13 | 38 |  | addi x20,x0,56 | 

## Slide 17: Instr. Mem.(2)
NO. | Instruction | Addr. | Label | ASM | Comment
15 | 03c00a13 | 3C |  | addi x20,x0,60 | 
16 | 00004537 | 40 | label0: | lui x10,4 | 
17 | 014005ef | 44 |  | jal x11,20 | 
18 | 04800a13 | 48 |  | addi x20,x0,72 | 
19 | 04c00a13 | 4C |  | addi x20,x0,76 | 
20 | 05000a13 | 50 |  | addi x20,x0,80 | 
21 | 05400a13 | 54 |  | addi x20,x0,84 | 
22 | ffff0617 | 58 |  | auipc x12, 0xffff0 | 
23 | 0223c6b3 | 5C |  | div x13, x7, x2 | 
24 | 02520733 | 60 |  | mul x14, x4, x5 | 
25 | 022687b3 | 64 |  | mul x15, x13, x2 | 
26 | 00400813 | 68 |  | addi x16, x0, 4 | 
27 | 000008e7 | 6C |  | jalr x17,0(x0) | 
Notes: 887 963=76/2=38
979-963=16

## Slide 18: Data Mem.
NO. | Data | Addr. | Comment
0 | 000080BF | 0 | 
1 | 00000008 | 4 | 
2 | 00000010 | 8 | 
3 | 00000014 | C | 
4 | FFFF0000 | 10 | 
5 | 0FFF0000 | 14 | 
6 | FF000F0F | 18 | 
7 | F0F0F0F0 | 1C | 
8 | 00000000 | 20 | 
9 | 00000000 | 24 | 
10 | 00000000 | 28 | 
11 | 00000000 | 2C | 
12 | 00000000 | 30 | 
13 | 00000000 | 34 | 
14 | 00000000 | 38 | 
15 | 00000000 | 3C | 
NO. | Instruction | Addr. | Comment
16 | 00000000 | 40 | 
17 | 00000000 | 44 | 
18 | 00000000 | 48 | 
19 | 00000000 | 4C | 
20 | A3000000 | 50 | 
21 | 27000000 | 54 | 
22 | 79000000 | 58 | 
23 | 15100000 | 5C | 
24 | 00000000 | 60 | 
25 | 00000000 | 64 | 
26 | 00000000 | 68 | 
27 | 00000000 | 6C | 
28 | 00000000 | 70 | 
29 | 00000000 | 74 | 
30 | 00000000 | 78 | 
31 | 00000000 | 7C | 

## Slide 19: Test Bench
RV32core core(
.debug_en(1'b0),
.debug_step(1'b0),
.debug_addr(7'b0),
.debug_data(),
.clk(clk),
.rst(rst),
.interrupter(1'b0)
);
initial begin
clk = 0;
rst = 1;
#2 rst = 0;
end
always #1 clk = ~clk;
00000013
00402103
00802203
004100b3
fff08093
00c02283
01002303
01402383
402200b3
ffd50093
00520c63
00420a63
00000013
00000013
00000013
00000013
000040b7
00c000ef
00000013
00000013
00000013
00000013
ffff0097
0223c433
025204b3
022404b3
00400113
000000e7

## Slide 20: Simulation (1)

## Slide 21: Simulation (2)

## Slide 22: Simulation (3)

## Slide 23: Simulation (4)
IF
ID

## Slide 24: Simulation (5)
ID
FU

## Slide 25: Simulation (6)
WB
Next FU EN

## Slide 26: Simulation (7)

## Slide 27: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 28
Thanks!