## Slide 1: Computer Architecture Experiment
浙江大学计算机学院
2021年9月
Topic 1. Pipelined CPU supporting RISC-V
RVI32 Instructions

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Precaution
Checkpoints

## Slide 3: Experiment Purpose
Understand RISC-V RV32I instructions
Master the design methods of pipelined CPU executing RV32I instructions
Master the method of Pipeline Forwarding Detection and bypass unit design
Master the methods of 1-cycle stall of Predict-not-taken branch design
master methods of program verification of Pipelined CPU executing RV32I instructions

## Slide 4: Experiment Task
Design of Pipelined CPU executing RV32I instructions.
  Design datapath
  Design Bypass Unit
  Design CPU Controller
Verify the Pipelined CPU with program and observe the execution of program

## Slide 5: Pipelined CPU supporting execution of RV32I instructions

## Slide 6: Pipelined CPU supporting execution of RV32I instructions

## Slide 7: Pipelined CPU supporting execution of RV32I instructions

## Slide 8: Pipelined CPU supporting execution of RV32I instructions

## Slide 9: Pipelined CPU supporting execution of RV32I instructions

## Slide 10: Instruction Demo

## Slide 11: Data Hazard Causes Stalls

## Slide 12: Pipeline Forward to Avoid the Data hazard

## Slide 13: SW After LW

## Slide 14: Condition in Which Bypass Unit doesn’t work

## Slide 15: Pipeline Stalls

## Slide 16: Instruction Demo

## Slide 17: Execution result

## Slide 18: Methods of resolving Control hazards
Freeze or flush the pipeline
Predict-not-taken
Predict-taken
Delayed branch

## Slide 19: Freeze method

## Slide 20: Predict-not-taken

## Slide 21: Predict-taken method
60% of branch result is taken
Bring forward calculation of branch condition from MEM Stage to EX Stage, stall reduce from 3-cycle to 2-cycle.
Then bring forward from EX to ID, stall reduce from 2-cycle to 1-cycle.
1-cycle stall may be used for 1 delay slot

## Slide 22: Stalls of Predict Methods for Control Hazard
Predict Methods | Status | Original Datapath | Address Calculation Forward | Condition Comparison Forward
Predict-taken | Hit (Need Branch) | 3 stall | 1 stall | 1 stall
Predict-taken | Miss (No Branch) | 3 stall | 3 stall | 1 stall
Predict-not-taken | Hit (No Branch) | go on | go on | go on
Predict-not-taken | Miss (Need Branch) | 3 stall | 3 stall | 1 stall

## Slide 23: Pipelined CPU supporting RV32I instructions

## Slide 24: Pipelined CPU supporting RV32I instructions

## Slide 25: Pipelined CPU supporting RV32I instructions

## Slide 26: Pipelined CPU supporting RV32I instructions

## Slide 27: Instr. Mem.(1)
NO. | Instruction | Addr. | Label | ASM | Comment
0 | 00000013 | 0 | __start: | addi x0, x0, 0 | 
1 | 00402103 | 4 |  | lw x2, 4(x0) | 
2 | 00802203 | 8 |  | lw x4, 8(x0) | 
3 | 004100b3 | C |  | add x1, x2, x4 | 
4 | fff08093 | 10 |  | addi x1, x1, -1 | 
5 | 00c02283 | 14 |  | lw x5, 12(x0) | 
6 | 01002303 | 18 |  | lw x6, 16(x0) | 
7 | 01402383 | 1C |  | lw x7, 20(x0) | 
8 | 402200b3 | 20 |  | sub x1,x4,x2 | 
9 | 002270b3 | 24 |  | and x1,x4,x2 | 
10 | 002260b3 | 28 |  | or x1,x4,x2 | 
11 | 002240b3 | 2C |  | xor x1,x4,x2 | 
12 | 002210b3 | 30 |  | sll x1,x4,x2 | 
13 | 002220b3 | 34 |  | slt x1,x4,x2 | 
14 | 004120b3 | 38 |  | slt x1,x2,x4 | 

## Slide 28: Instr. Mem.(2)
NO. | Instruction | Addr. | Label | ASM | Comment
15 | 002350b3 | 3C |  | srl x1, x6, x2 | 
16 | 402350b3 | 40 |  | sra x1, x6, x2 | 
17 | 4023d0b3 | 44 |  | sra x1, x7, x2 | 
18 | 007330b3 | 48 |  | sltu x1, x6, x7 | 
19 | 0063b0b3 | 4C |  | sltu x1, x7, x6 | 
20 | 00000033 | 50 |  | add x0,x0,x0 | 
21 | ffd50093 | 54 |  | addi x1,x10,-3 | 
22 | 00f27093 | 58 |  | andi x1,x4,15 | 
23 | 00f26093 | 5C |  | ori x1,x4,15 | 
24 | 00f24093 | 60 |  | xori x1,x4,15 | 
25 | 00f22093 | 64 |  | slti x1,x4,15 | 
26 | 00121093 | 68 |  | slli x1,x4,1 | 
27 | 00225093 | 6C |  | srli x1,x4,2 | 
28 | 40c35093 | 70 |  | srai x1, x6, 12 | 
29 | fff33093 | 74 |  | sltiu x1, x6, -1 | 

## Slide 29: Instr. Mem.(3)
NO. | Instruction | Addr. | Label | ASM | Comment
30 | fff3b093 | 78 |  | beq x4,x5,label0 | 
31 | 00520863 | 7C |  | beq x4,x4,label0 | 
32 | 00420663 | 80 |  | addi x0,x0,0 | 
33 | 00000013 | 84 |  | addi x0,x0,0 | 
34 | 00000013 | 88 | label0: | bne x4,x4,label1 | 
35 | 00421863 | 8C |  | bne x4,x5,label1 | 
36 | 00521663 | 90 |  | addi x0,x0,0 | 
37 | 00000013 | 94 |  | addi x0,x0,0 | 
38 | 00000013 | 98 | label1: | blt x5,x4,label2 | 
39 | 0042c863 | 9C |  | blt x4,x5,label2 | 
40 | 00524663 | A0 |  | addi x0,x0,0 | 
41 | 00000013 | A4 |  | addi x0,x0,0 | 
42 | 00000013 | A8 | label2: | bltu x6,x7,label3 | 
43 | 00736863 | AC |  | bltu x7,x6,label3 | 
44 | 0063e663 | B0 |  | addi x0,x0,0 | 
Addr Label ASM向下移动一格

## Slide 30: Instr. Mem.(4)
NO. | Instruction | Addr. | Label | ASM | Comment
45 | 00000013 | B4 |  | addi x0,x0,0 | 
46 | 00000013 | B8 | label3: | bge x4,x5,label4 | 
47 | 00525863 | BC |  | bge x5,x4,label4 | 
48 | 0042d663 | C0 |  | addi x0,x0,0 | 
49 | 00000013 | C4 |  | addi x0,x0,0 | 
50 | 00000013 | C8 | label4: | bgeu x7,x6,label5 | 
51 | 0063f863 | CC |  | bgeu x6,x7,label5 | 
52 | 00737663 | D0 |  | addi x0,x0,0 | 
53 | 00000013 | D4 |  | addi x0,x0,0 | 
54 | 00000013 | D8 | label5: | bge x4,x4,label6 | 
55 | 00425663 | DC |  | addi x0,x0,0 | 
56 | 00000013 | E0 |  | addi x0,x0,0 | 
57 | 00000013 | E4 | label6: | lui x1,4 | 
58 | 000040b7 | E8 |  | jal x1,12 | 
59 | 00c000ef | EC |  | addi x0,x0,0 | 

## Slide 31: Instr. Mem.(5)
NO. | Instruction | Addr. | Label | ASM | Comment
60 | 00000013 | F0 |  | addi x0,x0,0 | 
61 | 00000013 | F4 |  | lw x8, 24(x0) | 
62 | 01802403 | F8 |  | sw x8, 28(x0) | 
63 | 00802e23 | FC |  | lw x1, 28(x0) | 
64 | 01c02083 | 100 |  | sh x8, 32(x0) | 
65 | 02801023 | 104 |  | lw x1, 32(x0) | 
66 | 02002083 | 108 |  | sb x8, 36(x0) | 
67 | 02800223 | 10C |  | lw x1, 36(x0) | 
68 | 02402083 | 110 |  | lh x1, 26(x0) | 
69 | 01a01083 | 114 |  | lhu x1, 26(x0) | 
70 | 01a05083 | 118 |  | lb x1, 27(x0) | 
71 | 01b00083 | 11C |  | lbu x1, 27(x0) | 
72 | 01b04083 | 120 |  | auipc x1, 0xffff0 | 
73 | ffff0097 | 124 |  | jalr x1,0(x0) | 
74 | 000000e7 | 128 |  |  | 

## Slide 32: Data Mem.
NO. | Data | Addr. | Comment
0 | 000080BF | 0 | 
1 | 00000008 | 4 | 
2 | 00000010 | 8 | 
3 | 00000014 | C | 
4 | FFFF0000 | 10 | 
5 | 0FFF0000 | 14 | 
6 | FF000F0F | 18 | 
7 | F0F0F0F0 | 1C | 
8 | 00000000 | 20 | 
9 | 00000000 | 24 | 
10 | 00000000 | 28 | 
11 | 00000000 | 2C | 
12 | 00000000 | 30 | 
13 | 00000000 | 34 | 
14 | 00000000 | 38 | 
15 | 00000000 | 3C | 
NO. | Instruction | Addr. | Comment
16 | 00000000 | 40 | 
17 | 00000000 | 44 | 
18 | 00000000 | 48 | 
19 | 00000000 | 4C | 
20 | A3000000 | 50 | 
21 | 27000000 | 54 | 
22 | 79000000 | 58 | 
23 | 15100000 | 5C | 
24 | 00000000 | 60 | 
25 | 00000000 | 64 | 
26 | 00000000 | 68 | 
27 | 00000000 | 6C | 
28 | 00000000 | 70 | 
29 | 00000000 | 74 | 
30 | 00000000 | 78 | 
31 | 00000000 | 7C | 

## Slide 33: Simulation (1)
lw x2, 4(x0)
lw x4, 8(x0)
add x1, x2, x4
stall
X2 forwarding
X4 forwarding

## Slide 34: Simulation (2)

## Slide 35: Simulation (3)

## Slide 36: Simulation (4)
beq x4,x5,label0
beq x4,x4,label0
Predict not taken
Jump to label0
flush

## Slide 37: Simulation (5)

## Slide 38: Simulation (6)

## Slide 39: Simulation (7)

## Slide 40: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 41
Thanks!